| STRAW BURNING, WOOD BURNING AND BIOMASS BOILERS |  |
| --- | --- |

BIOWAT Boilers

These are batch boilers designed to heat residential houses and business facilities, having a surface area of up to 900m2. They heat, using wood and straw without the need to install accumulation tanks. The boilers burn fuel slowly. The combustion rate is manually adjusted via an air damper. The boilers work on natural draught.

The exit fuel chamber is fully clad with fireclay bricks. Gases flow from the fuel chamber through a burner to an upper, ceramic combustion chamber. Primary air is mixed with secondary air in the burner. With the combustion chamber, the exhaust gas flows into the box-exchanger.

Biowat burners are mounted directly onto the existing system instead of, or parallel with, the coal boiler. The boiler operates in the mandatory ‘open’ system.

"U" boilers are wood-burning. Straw may, however, be used - with the provision that a bale measures 80x45x40 cm. These can be installed in the basement. They then operate gravitationally, without a circulation pump. Their primary fuel is wood. U-300 boilers are capable of burning wood up to 6m in length. The U-360 to U-1100 boilers can take "wood-pulp" with a length of up to 1.2 m.

The basic fuel for "S" boilers is straw. During average winter temperatures, the boilers are loaded with fuel twice per 24 hours. Such as a 250m2 house will need the straw yielded by an area between 4.5 ha - 5 ha per year.

Ash removal should be carried out every few days. Ash is a phosphorus-potassium fertiliser.

The boilers can be loaded with fuel having up to 20% humidity; neither the species of the wood nor the use of tree stumps is of any consequence, however, the burning of sawdust only is not allowed; it must be mixed with, or put on top of, the straw. The boiler may be re-fuelled whilst in operation.

| Type of Boiler | L | H | L1 | H1 | D | Fuel chamber | Weight [kg] | Surface heated [m2] | Power [kw] | Net price [PLN] |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | G | W | S | Capacity [l] |  |  |  |  |
| 1470 | 898 | 1482 | 1200 | 1135 | 250 | 926 | 530 | 546 | 245 | 1000 | 200 | 25 | 8 350 |
| 1525 | 898 | 1482 | 1325 | 1135 | 250 | 1050 | 530 | 546 | 300 | 1100 | 250 | 28 | 9 150 |
| 1795 | 898 | 1482 | 1525 | 1135 | 250 | 1250 | 530 | 546 | 360 | 1250 | 280 | 32 | 9 600 |
| 1525 | 1112 | 1482 | 1325 | 1135 | 250 | 1050 | 530 | 760 | 420 | 1300 | 400 | 40 | 10 300 |
| 1915 | 1234 | 1652 | 1576 | 1156 | 320 | 1250 | 560 | 858 | 600 | 2000 | 500 | 60 | 14 150 |
| 2035 | 1330 | 1732 | 1650 | 1342 | 320 | 1250 | 730 | 900 | 820 | 2600 | 600 | 80 | 16 000 |
| 1775 | 1485 | 2100 | 1610 | 1930 | 320 | 1250 | 800 | 1100 | 1100 | 3200 | 800 | 100 | 18 300 |
| 1470 | 1402 | 1892 | 1200 | 1545 | 250 | 926 | 934 | 1050 | 4 bales of straw | 1800 | 200 | 25 | 13 300 |
| 1870 | 1402 | 1892 | 1600 | 1545 | 250 | 1326 | 934 | 1050 | 6 bales of straw | 2200 | 250 | 30 | 15 050 |

# Text boxes

CLEANOUT

Burner chamber

Combustion chamber